## Slide 1
This work was supported in part by Hewlett-Packard Labs, Palo Alto, CA; US Department of Energy (DOE); IARPA and C-BRIC, one of six centers in JUMP, a Semiconductor Research Corporation (SRC) program sponsored by DARPA.
PUMA: A Programmable Ultra-efficient Memristor-based Accelerator for Machine Learning Inference
Aayush Ankit*, Izzat El Hajj††, Sai Rahul Chalamalasetti†, Geoffrey Ndu†, Martin Foltin†, R. Stanley Williams†, Paolo Faraboschi†, Wen-mei Hwu††, John Paul Strachan†, Kaushik Roy*, Dejan Milojicic†
*Purdue University, † †University of Illinois at Urbana-Champaign, †Hewlett Packard Enterprise
Acknowledgments
Motivation for Hybrid Memristor-CMOS Architecture
PUMA CORE – Heterogeneous Execution
Results – Comparison with CPU, GPU, TPU
ML App Characteristic | MLP | LSTM | CNN | Memristor Feature
MVM Domination |  |  |  | Analog dot-product
Memory Bound |  |  | × | On-die, In-memory
Chart: 
| CNN (Lenet5) | MLP (64-150-150-14) | LSTM (26-120-61) | RNN (26-93-61) | BM (V500-H500) | RBM (V500-H500)
Inter-Tile Data Transfer | 0.059701 | 0.17391 | 0.17073 | 0.30769 | 0.076923 | 0.081633
Inter-Core Data Transfer | 0.35821 | 0.3913 | 0.39024 | 0.38462 | 0.42308 | 0.40816
Control Flow | 0.059701 | 0 | 0 | 0 | 0 | 0
Scalar Functional Unit | 0.23881 | 0 | 0 | 0 | 0 | 0
Vector Functional Unit | 0.19403 | 0.26087 | 0.31707 | 0.15385 | 0.34615 | 0.34694
MVM Unit (crossbar) | 0.089552 | 0.17391 | 0.12195 | 0.15385 | 0.15385 | 0.16327
MVM alone cannot execute ML apps
Memristor is a natural fit for ML app characteristics
Key memristor features:
  Ultra-high storage density (~160MB/mm2)
  Analog dot-product (Ohm’s law, KCL)
  High write cost (latency, energy)
Domain-specific ISA for ML for memristive systems
  Low decoder overhead
  Programmability
Co-locate different types of execution units: MVMU, VFU, ROM-Embedded RAM
  Near/In-memory processing
  General-purpose
Bit-streamed, weight-sliced MVMU: storage density - 2.72 MB/mm2
Exploits available ILP with MVM Coalescing
PUMA Multi-Core
Dataflow (spatial) architecture
  stationary weights and instructions
  data movement from partial sums and neurons, between cores
  Preserve storage density of memristor, to map models with on-chip memory only
  1 PUMA Node key metrics : 69 MB storage, 90 mm2, 577GOPS/mm2, 837 GOPS/W
Chart: Normalized Energy (lower is better)
| L4 | L5 | L3 | L5 | Big LSTM | LSTM- 2048 | Vgg16 | Vgg19 | MLP | Deep LSTM | Wide LSTM | CNN
Skylake | 10335.7229 | 8107.35 | 1151807.6059 | 1386359.594 | 790945.0805 | 1902526.5217 | 2454.4855 | 2716.9034
Pascal | 80.0469 | 30.2069 | 2302.4498 | 2445.5239 | 757.9461 | 1335.6647 | 12.9913 | 11.714
PUMA | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: Normalized Latency (lower is better)
| L4 | L5 | L3 | L5 | Big LSTM | LSTM- 2048 | Vgg16 | Vgg19 | MLP | Deep LSTM | Wide LSTM | CNN
Skylake | 11.4958 | 28.218 | 5362.2151 | 9543.7592 | 2061.912 | 2559.1796 | 231.1721 | 279.3917
Pascal | 0.40235 | 0.24169 | 41.6272 | 66.02 | 5.2421 | 4.7027 | 2.7277 | 2.9923
PUMA | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Compiler And Simulator
PUMA compiler – converts high level C++ code to PUMA assembly.
  Programmability: run large-scale models on 1000s of spatial cores
  Graph Partitioning (data movement optimization), register allocation, MVM Coalescing (ILP)
PUMAsim – power, performance, and functional simulator
  Enables ISA and architecture validation, design-space exploration
Chart: PUMA vs TPU
| GOPS/mm2 | GOPS/W
 | 8.3 | 9.6
*Skylake (14nm), PASCAL (16nm) and TPU (28nm) are board-level measurements, PUMA (32nm) results are simulation-level measurements.