## Slide 1: OASIS: Optimal Allocation Strategy for Inference Services in Cloud Environments
Viyom Mittal, Mohammed Baydoun, Alok Mishra, Pavana Prakash, Gourav Rattihalli, Aditya Dhakal, Eitan Frachtenberg, Izzat El Hajj, Michalis Faloutsos, Dejan Milojicic

## Slide 2
How can a cloud provider optimize resource use in providing language model as services?
High Energy Consumption: GPUs draw high power even when idle
Variable Query Traffic: GPUs draw high power even when idle; millions of daily requests compound costs
Query Heterogeneity: Different queries have vastly different resource needs
Multi-Tenancy: Must share GPUs efficiently; time-slicing vs MIG vs Software Batching
Goal: Minimize total operational cost (hardware + energy) while meeting all SLO constraints

## Slide 3: OASIS: Two-Phase Methodology
Phase 1: Pre-Deployment Profiling
Profile model across
      - Query types
      - Hardware configs
      - GPU frequencies
      - Batch sizes
Phase 2: Runtime Query Routing & Provisioning
- Classify incoming queries
- Compute GPU requirements
- Decide MIG vs. Full GPU
- Dynamically provision

## Slide 4
Query Type Classification (τ = 500 tokens)
 | Small Output (< τ) | Large Output (> τ)
Small Input (< τ) | SISO: Short Q&A, paraphrasing (minimal compute) | SILO: Story generation, essays (memory-intensive generation)
Large Input (> τ) | LISO: Summarization, classification (compute-intensive prefill) | LILO: Translation, long rewriting (intensive throughout)

## Slide 5
Phase 1: Pre-Deployment Profiling
Profiling Procedure:
Define parameter space:
          - GPU freq {855-1410 MHz}
          - Batch {16-64}
          - Variants {standard, prefix-caching, chunked-prefill}
2. Sweep each query type (LISO, SILO) separately
3. For each parameter dimension, vary one parameter while keeping others fixed.
3. Ramp concurrency from low → high
4. Measure P95 latency, throughput, power, energy/token
5. Determine Max Serviceable Request Rate meeting SLO
6. Record MSRR, Power and energy/token in the Hardware Cost Table (HCT)

## Slide 6
Phase 1: Experiments
Aim: Study impact of query type on throughput
Setup:
SLO: P95 should be less than 20 seconds
Constants: GPU (A100), frequency (default 1410MHz), model (Llama3-8B, Qwen-7B)
Variables: Query type (LISO vs SILO), concurrency (ramp until SLO violated)
Observation 1: LISO achieves **2.1× higher throughput** than SILO.
Observation 2: Qwen-7B has **1.5× higher LISO throughput** than Llama3-8B.
Takeaway: Per-model, per-query-type profiling is essential

## Slide 7
Phase 1: Experiments
Aim: Study impact of GPU frequency reduction on throughput
Setup:
SLO: P95 should be less than 20 seconds
Constants: model (Llama-3-8B), GPU (A100)
Variables: GPU frequency {1320, 1035, 855} MHz
Observation: Reducing frequency from 1320→855 MHz: 39% power reduction with only 7% decrement in throughput
Takeaway: Frequency tuning can result in major cost savings with minimal throughput reduction

## Slide 8
Phase 1: Experiments
Aim: Hardware Platform Comparison (A100 vs H100)
Setup:
SLO: P95 should be less than 20 seconds
Constants: model (Yi-6B), SLO (20s)
Variables: GPU platform (A100 vs H100), frequency
Observation: H100 provides **+12% throughput** but consumes **+89% more power** vs A100
Takeaway: Hardware selection requires workload and model specific analysis

## Slide 9
Phase 1: Experiments
Aim: Study cross-Model Energy Efficiency
Observation: 1.4× energy across models at identical GPU frequency.
Aim: Determine if MIG-based GPU sharing can reduce power when serving multiple models simultaneously
Observation: MIG achieves **42–43% power reduction** (saves 197W) for LISO workload
Takeaway: Architecture matters more than just parameter count. Per-model profiling remains essential.
Takeaway: Scale down can help in power savings when dealing with SLMs.

## Slide 10
Phase 2: Runtime Adaptation Algorithm

## Slide 11
Phase 2: Real campus workload evaluation
Setup:
A100-80GB: Full GPU vs. MIG (half GPU)
vLLM v0.6.3 + Meta-Llama-3-8B-Instruct
BurstGPT dataset: 4-hour daytime trace, 153 requests
Bursty traffic: CV = 1.70
Query distribution:
SISO: 64.7%
SILO: 5.9%
LISO: 29.4%
LILO: 0%
94.1% queries have small output.

## Slide 12
Phase 2: Real campus workload evaluation
Observations:
The MIG configuration maintains identical throughput
TTFT and E2E latency increase but remain within acceptable bounds
Mean power consumption reduces by 12.4%.
Takeaway: Significant power savings can be achieved while remaining SLO compliant.

## Slide 13
Conclusion
Each parameter reveals actionable optimization opportunities:
GPU Frequency: Most impactful knob: −39% power, −7% throughput, +34% energy efficiency
Query Type: LISO sustains 2.1× higher throughput than SILO; uniform provisioning wastes resources or violates SLOs
Model Architecture: 1.4× energy variation (86.1–118.4 mJ/tok) across 7B-15B models at identical hardware settings
Hardware Platform: Not always "bigger is better": H100 gives +12% throughput but costs +89% power vs A100 - Highly traffic dependent
Deployment Strategy (MIG vs Full GPU): 12.4% power reduction on real campus trace
Future work:
Multi-parameter joint optimization
Workload prediction & proactive adaptation
Cross-GPU architecture support

## Slide 14: Thank you!
For follow-up questions:
viyom.mittal@hpe.com