## Slide 1: PUMA: A Programmable Ultra-efficient Memristor-based Accelerator for Machine Learning Inference
Aayush Ankit1,3, Izzat El Hajj2,4, Sai Rahul Chalamalasetti3, Geoffrey Ndu3, Martin Foltin3, R. Stanley Williams3, Paolo Faraboschi3, Wen-mei Hwu4, John Paul Strachan3, Kaushik Roy1, Dejan S Milojicic3
Purdue University1
American University of Beirut2
Hewlett Packard Enterprise3
University of Illinois at Urbana-Champaign4

## Slide 2: Motivation: Human vs. Machine Chronicles
IBM Deep Blue vs. Kasparov
IBM RS/6000 32-node server
~15000W
IBM Watson vs. Ritter & Jennings
90 Power 750 Express servers ~200000W
Google AlphaGo vs. Sedol
(1920 CPUs, 280 GPUs)
~300000W
1997
2011
2016
Algorithm performance moving closer
Hardware cost moving farther
“Aspirations have grown faster than the technology available to satisfy them”.

## Slide 3: Motivation: Need to Look Beyond CMOS Digital Accelerators
Ref: IBM AI Hardware Research (https://www.ibm.com/blogs/research)
Analog PIM
Industrial presence
ML models are growing faster than CMOS hardware.

## Slide 4: Background: Memristive Crossbars
Memory aspects:
High Density + On-Die Storage
Tunable Resistance
Compact cell structure
States
Memristor = Memory + Resistor
Array Density: 160MB/mm2
Mitigates off-chip data access
>100×
Cell area is 4F2 vs 120F2 for CMOS (SRAM).
30×
2-6 bits per cell vs 1-bit for CMOS (SRAM).
6×

## Slide 5: Background: Memristive Crossbars
V
G
Compute Aspects:
Analog Multiplication
V0
V1
V2
V3
G0
G1
G2
G3
Analog Dot Product
V0
V1
V2
V3
G0,0
G0,1
G0,2
G0,3
G1,0
G1,1
G1,2
G1,3
G2,0
G2,1
G2,2
G2,3
G3,0
G3,1
G3,2
G3,3
Analog Matrix Vector Multiplication (MVM)
Analog MVM: 1.34pJ/op*
Efficient compute
>4×
*32nm technology

## Slide 6: Background: Past Memristive Based Accelerators
DAC
DAC
DAC
DAC
INT
INT
INT
INT
Multiplexer
ADC
Shift-&-Add
MVM Unit (MVMU):
Add peripherals to interface crossbar with digital domain.
Past accelerators: RENO [DAC’15], ISAAC and PRIME [ISCA’16] achieve significant benefits over CMOS accelerators for limited applications (1 or 2).
Memristive crossbars are not drop-in replacement of traditional memory structures (Cache, Register File).
  General purpose ML architecture ? 
  Programmability ? 
PUMA is the first general-purpose and programmable accelerator with memristive crossbars.

## Slide 7: PUMA Architecture: Spatial scalability
Expensive writes
  writes consume orders of magnitude more energy/latency than CMOS (SRAM)
Limited endurance
  typically 10^9 writes, CMOS has infinite endurance
Chart: Energy Cost
| MVM | Memory Read | Memory Write
CMOS | 146.3837 | 302.3256 | 302.3256
ReRam | 35.104 | 280.832 | 2949.12
Costly writes to memristive crossbars are alleviated in spatial architecture
  Model doesn’t change during inference (trained once, millions of inference)
High storage density enables spatial architecture
  State-of-the-art apps can be mapped in ~GPU die area, if the high storage density can be retained at system-level

## Slide 8: PUMA Architecture: Spatial scalability
Data
Memory Controller
Attribute Buffer
Instruction Memory
Write mux
Read mux
FIFO
FIFO
Tile Control Unit
Receive Buffer
to/from Router
Shared Memory
CORE 0
CORE 1
CORE 2
CORE 4
CORE N
PUMA Tile
(Multi-core with Shared Memory)

## Slide 9: PUMA Architecture: Spatial scalability
Network on Chip
Massively parallel accelerator –> Amenable to Data-Level Parallelism -> Highly efficient ML inference

## Slide 10: Key challenges
Enable general-purpose and programmable architecture while preserving the crossbar storage density
  Memristive technology has orders of magnitude higher area-efficiency than CMOS technology, for both storage and compute
  Storage density drops from 160MB/mm2 at array-level to 2.6MB/mm2 at MVMU-level (ISAAC, ISCA’16) !!!
Optimize data movements
  Weights remain stationary, but partial sums and activations lead to data movements
  Spatiality incurs high cost for data movement between cores
Proposal: Architecture-ISA-Compiler codesign.

## Slide 11: Contribution 1: Domain-specific ISA
Large variety of ML workloads
  Support Vector Machines
  Neural Networks (>27)
  …
State machine approach to represent a functional block, leads to high decoding overheads when scope of workloads is large
So many workloads, share many low-level operations
ISA for ML for memristive architecture
  Fine grain instructions compose to make an ML workload
  Low area-overhead decoder and programmability
http://www.asimovinstitute.org/neural-network-zoo/
*Figure shows partial list

## Slide 12: Contribution 1: Domain-specific ISA
Compute
Data Move
(Intra-Tile)
Control
Data Move
(Inter-Tile)
Compute
Data Move (Intra-Tile): over shared bus, shared memory
Control: loops in workloads with MVMU reuse (weight reuse)
Data Move (Inter-Tile): over network on chip.
Wide instructions
  Large register address space to support memristive crossbars (very-wide SIMD)
  vector width keeps instruction memory low in spatial architecture

## Slide 13: Contribution 1: Domain-specific ISA
LD $mi1, x, n
MVM 0b01
ALU_SIG $1, $mo1, n
ST $1, a
a
z
x
PUMA Core
MVM 0b01
// for all partial sums
LD xxx // bring partial sums from other cores
ALU_ADD xxx // accumulate partial sums
ALU_SIG $1, $mo1, n
MLP maps on one MVMU
MLP maps on multiple MVMUs/Cores
1 Layer MLP
Larger matrices require more data movements to compute effective MVM.

## Slide 14: Contribution 2: Hybrid Core
MVMU alone cannot execute ML apps.
  Vector operations: require previous writes to crossbar
  Transcendental operations: MVMU (even with writes) can do add/multiply only.
Propose core designed with hybrid memristive and CMOS technologies.
  Hybrid analog-digital core: general-purpose
  Co-locating execution units reduces data movements (near-memory)
z
x
1 Layer LSTM
ht
ct
ht+1
3 Vector Multiply
1 Vector Add
2 Tanh
1 Sigmoid
Chart: 
| CNN (Lenet5) | MLP (64-150-150-14) | LSTM (26-120-61) | RNN (26-93-61) | BM (V500-H500) | RBM (V500-H500)
Inter-Tile Data Transfer | 0.059701 | 0.17391 | 0.17073 | 0.30769 | 0.076923 | 0.081633
Inter-Core Data Transfer | 0.35821 | 0.3913 | 0.39024 | 0.38462 | 0.42308 | 0.40816
Control Flow | 0.059701 | 0 | 0 | 0 | 0 | 0
Scalar Functional Unit | 0.23881 | 0 | 0 | 0 | 0 | 0
Vector Functional Unit | 0.19403 | 0.26087 | 0.31707 | 0.15385 | 0.34615 | 0.34694
MVM Unit (crossbar) | 0.089552 | 0.17391 | 0.12195 | 0.15385 | 0.15385 | 0.16327

## Slide 15: Contribution 2: Hybrid Core
(déjà vu) Preserving storage density - Memristive and CMOS technology have orders of magnitude disparity in area-efficiency.
Decoded
instruction
ALU_ADD $d1, $s1, $s2, n
Temporal SIMD
  Low width VFU saves area
  Wide vector instruction have low fetch/decode/instruction storage overhead
VFU needs to be fast enough to not be a bottleneck for MVMU
  ML workloads: all other operations (vector, transcendental) are preceded by MVM
A[1] = B[1] + C[1]
A[0] = B[0] + C[0]

## Slide 16: Contribution 2: Hybrid Core
Register file buffers operands and becomes an on-demand transcendental function unit (sig, tanh, etc.)
Multiple cycles (2-3), needs to be fast enough for MVMU.
Add an extra worldline to every row (~1% array area overhead, sense-amps unchanged)
RAM: Activate both wordlines - WL1 and WL2
ROM: storage depends on AXL’s connection to wordline WL1
  Write 0s (both wordline active)
  Selectively write 1s (WL1 active)
  Read data (typical RAM read)
  Restore RAM data (ROM read is destructive)

## Slide 17: Contribution 3: Compiler optimizations
Programmability: traditional programming models not suitable for spatial architecture.
Writing different code for each core/tile is not scalable as applications grow.
Optimizations:
  Graph partitioning: optimizing for data movements
  MVM Coalescing: extract available ILP
Compiler

## Slide 18: Contribution 3: Compiler optimizations
Data movement is analogous to memory hierarchy in traditional systems, highest contributor in energy profile.
First level of graph partitioning, optimizing for locality and inter-core communication (LD/ST).
Second level of graph partitioning, optimizing for locality and inter-tile communication (Send/Receive).
CORE 0
CORE 1
MVM
MVM
CORE N
CORE N+1
MVM
MVM
Chart: 
| Intra-core | Inter-core | Inter-tile
 | 0.954 | 3.009 | 18.045
Send/Receive
LD/ST
LD/ST
Tile 0
Tile N

## Slide 19: Contribution 3: Compiler optimizations
MVM instructions consume high latency
MVM Coalescing
  Schedule the required LDs, coalesce the MVMs
Area-efficiency, alternatively score-boarding is too expensive.
Instruction | Cycles
LD/ST | >24
ALU | 128 - 384
MVM | 2304
Send/Receive | variable
LD $mi1, x, n
MVM 0b01
ALU_SIG $1, $mo1, n
ST $1, a
LD $mi2, x, n
MVM 0b10
ALU_SIG $2, $mo2, n
ST $2, a
LD $mi1, x, n
LD $mi2, x, n
MVM 0b11
ALU_SIG $1, $mo1, n
ST $1, a
MVM 0b10
ALU_SIG $2, $mo2, n
ST $2, a

## Slide 20: Results: Inference Energy (Batch size = 1)
CNNs show upto 13.0× reduction (least).
  High weight reuse, even at batch-size 1.
MLPs show upto 80.1× reduction.
  No weight reuse, small models.
LSTMs show upto 2446× reduction.
  Little Weight reuse, large models (billions of parameters).
Chart: Normalized Energy (lower is better)
| L4 | L5 | L3 | L5 | Big LSTM | LSTM- 2048 | Vgg16 | Vgg19 | MLP | Deep LSTM | Wide LSTM | CNN
Skylake | 10335.7229 | 8107.35 | 1151807.6059 | 1386359.594 | 790945.0805 | 1902526.5217 | 2454.4855 | 2716.9034
Pascal | 80.0469 | 30.2069 | 2302.4498 | 2445.5239 | 757.9461 | 1335.6647 | 12.9913 | 11.714
PUMA | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PUMA achieves massive reduction in inference energy across all platforms for all benchmarks.

## Slide 21: ASIC Comparison
Google TPU comparison
Cost of generality, programmability
  20.7% lower power efficiency and 29.2% lower area efficiency than ISAAC.
Modest cost increase over past memristive accelerators, significantly improves applicability of memristive crossbars.
Chart: PUMA vs TPU
| GOPS/mm2 | GOPS/W
 | 8.3 | 9.6

## Slide 22: Conclusion
General-purpose
Programmability
Storage Density
Data Movement
Goals
Constraints
Domain Specific ISA
Domain Specific ISA
Hybrid Core
Hybrid Core
Compiler Optimizations
First general-purpose and ISA-programmable accelerator built with hybrid CMOS-Memristive technology.
  Architecture-ISA-Compiler Codesign
  Many other optimizations (input shuffling, spatial pipelining, inter-core synchronization, register allocation etc.) and detailed results in paper.
Compiler Optimizations

## Slide 23: Toolchain for Memristive Accelerators
PUMA Compiler
Integrated with Open Neural Network Exchange to execute models from various DNN frameworks
PUMA ISA
PUMA Simulator
github.com/illinois-impact/puma-compiler
github.com/Aayush-Ankit/puma-simulator
Questions?