## Slide 1
Predicting Performance Variability
Mohammed Baydoun (AUB), Mohammad Sonji (AUB), Pedro Bruel (HPE), Dejan Milojicic (HPE), Eitan Frachtenberg (HPE), Izzat El Hajj (AUB)
The International Workshop on Automatic Performance Tuning (iWAPT’25)
June 3, 2025

## Slide 2
Motivation: Computer Applications have Performance Variability

## Slide 3
Motivation: Many Samples are Needed to Measure an Accurate Distribution
Measured distribution from 1,000 samples
Measured distribution from 10 samples
Measured distribution from 2 samples
Measured distribution from 3 samples
Measured distribution from 5 samples

## Slide 4
What if we do not have the resources to run the application many times on the system?
  Can we predict the performance distribution from just a few samples?
  Can we predict the performance distribution from running on another system?
Train model by learning from other applications
Research Question
performance
density
Prediction Model
App
…

## Slide 5
Sneak Peak at Results
Measured distribution from 1,000 samples
Predicted distribution from 10 samples
Measured distribution from 10 samples
Measured distribution from 2 samples
Measured distribution from 3 samples
Measured distribution from 5 samples

## Slide 6
Predicting Performance Distribution from Few Samples
Profiler
performance
density
Prediction Model
run | metrics |  |  |  |  | perfor-mance
 | m1 | m2 | m3 | … | mk | 
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
App
How to represent an application’s profile as a feature vector?
Which model to use?
What data to train it with?
How to represent a performance distribution as a feature vector?

## Slide 7
Predicting Performance Distribution from Few Samples
Profiler
performance
density
Prediction Model
run | metrics |  |  |  |  | perfor-mance
 | m1 | m2 | m3 | … | mk | 
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
App
How to represent an application’s profile as a feature vector?
Which model to use?
What data to train it with?
How to represent a performance distribution as a feature vector?

## Slide 8
Application-independent hardware and software metrics (68 metrics from from Linux perf)
  Instruction counts (branches, loads, stores, floating point, total)
  Cache metrics (references, hits, misses)
  Main memory metrics
  TLB metrics
Relative metrics normalized per second
  Unify model across applications with different durations
If multiple samples, mean, standard deviation, skewness, kurtosis
  Higher order moments did not improve results
Representing an Application’s Profile

## Slide 9
Predicting Performance Distribution from Few Samples
Profiler
performance
density
Prediction Model
run | metrics |  |  |  |  | perfor-mance
 | m1 | m2 | m3 | … | mk | 
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
App
How to represent an application’s profile as a feature vector?
Which model to use?
What data to train it with?
How to represent a performance distribution as a feature vector?

## Slide 10
Histogram: The feature vector is the bins of a histogram of the relative time (similar to a discretized PDF)
Moments: The feature vector is the moments of the distribution (we consider the first four moments: mean, standard deviation, skewness, and kurtosis)
  PyMaxEnt: Reconstruct the distribution from the moments using the principle of maximum entropy [30]
  PearsonRnd: Reconstruct the distribution by drawing random numbers from the distribution in the Pearson system with these moments
Representing the Performance Distribution

## Slide 11
Predicting Performance Distribution from Few Samples
Profiler
performance
density
Prediction Model
run | metrics |  |  |  |  | perfor-mance
 | m1 | m2 | m3 | … | mk | 
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
App
How to represent an application’s profile as a feature vector?
Which model to use?
What data to train it with?
How to represent a performance distribution as a feature vector?

## Slide 12
k-nearest neighbors (kNN)
  Can deal with noisy data, which is the case for the metrics we collect
  k = 15
  Distance metric: cosine similarity
Random forests (RF) and extreme gradient boosting (XGBoost)
  Can deal with a large and diverse set of input features
Choice of Prediction Model

## Slide 13
Predicting Performance Distribution from Few Samples
Profiler
performance
density
Prediction Model
run | metrics |  |  |  |  | perfor-mance
 | m1 | m2 | m3 | … | mk | 
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
App
How to represent an application’s profile as a feature vector?
Which model to use?
What data to train it with?
How to represent a performance distribution as a feature vector?

## Slide 14
Use 60 benchmarks from popular HPC and data analytics applications and libraries
Run application for 1,000 repetitions (samples) to measure the distribution
Training the Model

## Slide 15
Hardware specifications
  Intel Xeon Platinum 8358 CPU
  512GB of DDR4 RAM
  64 cores total (2 sockets, 32 cores per socket)
Benchmarking conditions
  The benchmarks ran on an entire node and without any interference
Error evaluation
  We use cross-validation (leave-one-group-out) to assess the accuracy of the model
  We use the Kolmogorov-Smirnov (KS) divergence test to assess quantify the agreement between the observed and predicted distributions (0 is a perfect match, 1 is the worst)
Evaluation Methodology

## Slide 16
Evaluation: Model and Output Representation
Observation #1: kNN has the lowest median KS score
Observation #2: PearsonRnd has the lowest median KS score
Observation #3: Most benchmarks have KS score lower than 0.4

## Slide 17
Evaluation: Number of Samples
Observation: Improved accuracy as number of samples increases
(users can trade off number of samples for accuracy)

## Slide 18
Evaluation: Examples
Observation #1: Width of the distribution predicted accurately
Observation #2: Number of modes and relative positions and sizes predicted accurately

## Slide 19
Same design considerations as the first use case
  Input distribution includes distribution of profiling metrics, not just perfomance
Hardware specifications of the second system used
  AMD EPYC 7543 CPU
  512GB of DDR4 RAM
  64 cores total (2 sockets, 32 cores per socket)
75 profiling metrics different from the ones on the Intel system
Predicting Performance Distributions from Another Distribution on Another System
Profiler
performance
density
Prediction Model
App
performance
density
System 1
System 2

## Slide 20
Evaluation: Model and Output Representation
Observation #1: kNN has the lowest median KS score
Observation #2: PearsonRnd has the lowest median KS score
Observation #3: Most benchmarks have KS score lower than 0.4

## Slide 21
Evaluation: Direction of Prediction
Observation: Prediction accuracy differs based on direction of prediction but only slightly

## Slide 22
Evaluation: Examples
Observation #1: Width of the distribution predicted accurately
Observation #2: Number of modes and relative positions predicted accurately, but mixed success on their relative sizes

## Slide 23
We show that application performance variability can be predicted by learning from other applications
We use application-independent profiling and relative profiling metrics to unify model across diverse applications with different durations
We show that kNN is the best performing model and PearsonRnd is the best method for representing the distribution for the purpose of prediction
Future work:
  Increase training data by covering more applications and systems
  Use explainable models and leverage explanations to optimize for variability
Summary and Future Work

## Slide 24
Predicting Performance Variability
Mohammed Baydoun (AUB), Mohammad Sonji (AUB), Pedro Bruel (HPE), Dejan Milojicic (HPE), Eitan Frachtenberg (HPE), Izzat El Hajj (AUB)
The International Workshop on Automatic Performance Tuning (iWAPT’25)
June 3, 2025